## Slide 1
IED UNIT 1 • LESSON 1.6
Measurement, Precision & Tolerances
How do engineers decide how accurately a part must be measured and manufactured?
DAY 1
MEASURE
Choose the right tool and record a realistic value.
DAY 2
CALCULATE
Turn nominal dimensions and tolerances into allowable limits.
DAY 2
INSPECT
Compare actual parts to engineering drawings and decide pass/fail.
The drawing defines the requirement. Measurement provides the evidence.

## Slide 2
DAY 1
Choose the Right Measuring Tool
Use only as much precision as the engineering decision requires.
BASIC
Ruler
Best for larger dimensions and quick checks. Resolution is limited by the smallest scale division.
PRECISION
Caliper
Useful for outside dimensions, inside dimensions, hole diameters, thicknesses, and depths.
METHOD
Good Technique
Keep the tool square to the feature, use consistent contact pressure, and read the same reference surfaces each time.
Do not add decimal places that the tool cannot support.

## Slide 3
DAY 1
Repeatability
Can you obtain nearly the same measurement again?
Measure the same feature three times.
Calculate the range
Range = largest measurement - smallest measurement A smaller range generally indicates more consistent measurement technique.
Look for sources of variation
Tool alignment • contact pressure • reference surfaces • reading error • surface texture • print artifacts
Consistency does not guarantee accuracy, but inconsistent measurements make inspection decisions difficult to defend.

## Slide 4
DAY 2
Tolerance Defines Acceptable Variation
Nominal ± Tolerance
LOWER LIMIT
nominal - tolerance
UPPER LIMIT
nominal + tolerance
DECISION
actual measurement must fall within the limits
Example: 0.500 ± 0.005 in → 0.495 to 0.505 in
Values exactly on the stated limits are acceptable unless the drawing says otherwise.

## Slide 5
DAY 2
Manufacturing Inspection Workflow
1
READ
Identify the required feature and dimension.
2
LIMITS
Calculate the lower and upper limits.
3
MEASURE
Use the appropriate tool and record the actual value.
4
DECIDE
Mark the feature PASS or FAIL.
5
DISPOSITION
Accept the part only if every required feature passes.
Do not decide from appearance.

## Slide 6
INSPECTION SET
Model A • Through Hole Block
MODEL A
WHAT TO INSPECT
Overall length Overall height Overall depth Hole diameter Horizontal hole location Vertical hole location
TOLERANCE PATTERN
Overall size: ± .020 in Hole location: ± .010 in Hole diameter: ± .005 in
KEY IDEA
A hole must be correct in both size and location. A correctly sized hole can still fail if its center is misplaced.
Use the engineering drawing as the requirement.

## Slide 7
INSPECTION SET
Models B & C
MODEL B • TWO LEVEL STAIR BLOCK
Inspect overall dimensions plus step runs and step heights. Related dimensions must all satisfy the drawing; one failed step feature rejects the part.
MODEL C • SLOTTED BRACKET
Inspect overall size, hole size and location, slot geometry, and thin wall/web features. Notice that the .090 wall/web and hole diameter use tighter tolerances than overall size.
Ask: Which dimensions are most critical to fit, alignment, or function?

## Slide 8
WRAP-UP
Your Inspection Must Be Defensible
A professional inspection decision connects three pieces of evidence:
REQUIREMENT
What dimension and tolerance does the drawing specify?
ACTUAL
What did you measure with an appropriate tool?
DECISION
Does the actual value fall within the allowable limits?
Complete your packet and make an ACCEPT / REJECT decision for each model.