## Slide 1
IED UNIT 1 • LESSON 1.7
Joining Methods & Assembly Systems
How do engineers choose the best way to connect parts in an assembly?
STEP 1
IDENTIFY
What joins the parts? What evidence shows that?
STEP 2
COMPARE
What does this method do better or worse than alternatives?
STEP 3
JUSTIFY
Which joining method best fits the interface requirements?
A good connection is selected for a reason.

## Slide 2
CORE IDEA
A joint is an engineering decision
Do not stop at naming the fastener.
CATEGORY
Mechanical Fasteners
Bolts, screws, washers, rivets, and pins can clamp, align, retain, or transfer load. Some are removable; others are not.
CATEGORY
Bonded & Fit-Based Joints
Adhesives and press fits can reduce hardware, but performance depends on material, surface area, process, and tolerances.
CATEGORY
Integrated Features
Tabs, slots, and snap fits use the part geometry itself. They can simplify assembly but may be harder to repair.
The interface requirement should drive the joining method.

## Slide 3
VOCABULARY
Removable, Semi-Permanent, Permanent
COMES APART
Removable
Designed to come apart with normal tools. Examples: bolt/nut, machine screw, access-panel fasteners.
SERVICE COST
Semi-Permanent
Can be removed, but removal may damage or replace a component. Example: rivet.
STAYS TOGETHER
Permanent
Not intended to come apart during normal use. Examples: adhesive joint, welded joint, some press fits.
Ask: should this connection be serviced later?

## Slide 4
DECISION FACTORS
Use multiple factors in your justification
Load
force, vibration, impact, repeated use
Serviceability
repair, replacement, inspection, adjustment
Alignment
precise location or orientation
Manufacturing
available tools, consistency, access
Cost / Complexity
hardware, labor, special steps
Permanence
easy to separate or never separated
Strong answers connect the joint to the requirements of the interface.

## Slide 5
LAB
Six Purpose-Made Joining Samples
Use the physical evidence to identify and evaluate each station.
Station A
Bolt + nut + washer
Station B
Screw into threads
Station C
Rivet
Station D
Adhesive lap joint
Station E
Press / friction fit
Station F
Tab/slot + snap feature
Return each sample assembled and ready for the next group.

## Slide 6
STATIONS A & B
Threaded Fasteners
A
Station A: Bolt + Nut + Washer
A fastener passes through both parts and is secured with a nut. This provides clamping and serviceability, but usually needs access to both sides.
B
Station B: Screw Into Threads
The fastener engages threads in one part, a threaded insert, or a captured nut. This can reduce loose hardware and may allow one-sided access.
Question: When would a bolt be better than a screw?

## Slide 7
STATIONS C & D
Permanent and Semi-Permanent Joints
C
Station C: Rivet
A rivet clamps overlapping parts quickly and compactly. It is difficult to service because the rivet is usually destroyed during removal.
D
Station D: Adhesive Lap Joint
A bonded overlap can spread load and avoid separate hardware. Strength depends on surface preparation, bond area, and process control.
Question: What do you gain and lose when you remove mechanical hardware?

## Slide 8
STATIONS E & F
Fit and Integrated Features
E
Station E: Press / Friction Fit
The fit depends on dimensions. A loose hole will not retain the pin; an overly tight hole may not assemble or may damage the part.
F
Station F: Tab/Slot + Snap Feature
Geometry locates and retains the parts. It can speed assembly, but flexible features may wear or break.
Connection to Lesson 1.6: dimensional control can determine whether a joint works at all.

## Slide 9
SELECTION CHALLENGE
Choose based on requirements, not preference
SCENARIO 1
Avionics Access Panel
Must be opened several times each year, experiences vibration, and should use a common hand tool.
SCENARIO 2
Thin-Sheet Bracket
Will not normally be serviced and should be quick and inexpensive to produce.
SCENARIO 3
Printed Sensor Housing
Must align quickly, use minimal hardware, and may be opened occasionally.
Use at least three decision factors in your justification.

## Slide 10
WRAP-UP
Make your engineering decision defensible
A complete joining-method recommendation includes:
Requirement
What must the interface accomplish?
Evidence
What do you observe in the sample?
Tradeoff
What is gained and what is lost compared with another method?
Submit the completed Connection Decision Lab packet.