## Slide 1
Introduction to Engineering Design
Unit 1: Technical Sketching & Engineering Documentation
Student learning deck • LockwoodSTEM aerospace-aligned IED curriculum
Module
Sketching, measurement, line conventions, views, and documentation.
Skills
Isometric sketching, orthographic projection, dimensioning, and reverse engineering.
Challenge
Document and propose improvements to a 3D printed rocket assembly.
Sketch • Measure • Document • Communicate

## Slide 2
LOCKWOODSTEM
Unit 1
Unit 1 Learning Arc
Technical sketching becomes engineering evidence when it is accurate, labeled, measured, and documented.
LockwoodSTEM | Introduction to Engineering Design | Unit 1
Lesson range | Focus | Purpose
1.1–1.6 | Sketching language | Use line types, isometric views, hidden lines, and centerlines to communicate shape.
1.7–1.10 | Views + dimensions | Use orthographic views and dimensions to describe size and geometry clearly.
1.11–1.20 | Rocket documentation | Reverse engineer a 3D printed rocket through sketches, measurements, BOM, and notes.
1.21–1.22 | Design proposal | Use evidence to propose a rocket assembly improvement and communicate it clearly.
Core idea
You are learning to communicate engineering decisions clearly enough that another person could inspect, build, or improve the design.

## Slide 3
LOCKWOODSTEM
Unit 1
Unit 1 Deliverables Map
You will build a documentation package, not just complete isolated sketches.
LockwoodSTEM | Introduction to Engineering Design | Unit 1
Checkpoint | Student evidence
Sketching practice | Line conventions, isometric views, hidden-line sketches, centerlines, and shading.
Technical views | Orthographic views, dimensions, bracket sketches, and measurement notes.
Rocket documentation | Reverse-engineering notes, parts list, exploded view, assembly notes, and BOM.
Final proposal | Engineering Change Request and rocket assembly improvement presentation.
Evidence expectation
Each artifact should be dated, labeled, and clear enough to stand alone as engineering evidence.

## Slide 4
LOCKWOODSTEM
Unit 1
How Unit 1 Works
Every lesson should improve the evidence you can use later.
LockwoodSTEM | Introduction to Engineering Design | Unit 1
What you are practicing
First, learn the visual language engineers use to communicate shape and structure.
Next, apply that language to aerospace-style parts and rocket components.
Then, combine sketches, measurements, views, and notes into a complete documentation package.
Finally, use your evidence to justify one proposed improvement to the rocket assembly.
Remember
A good sketch is not judged by whether it is artistic. It is judged by whether it communicates the design clearly.

## Slide 5
LOCKWOODSTEM
Lesson 1.1
Why Engineers Sketch
LockwoodSTEM | Introduction to Engineering Design | Unit 1
Why do engineers sketch before they build or model in CAD?
Lesson 1.1
Why Engineers Sketch
Connect today’s work to your engineering notebook evidence.

## Slide 6
LOCKWOODSTEM
Lesson 1.1
Why Engineers Sketch
Big ideas you should understand before you start the work
LockwoodSTEM | Introduction to Engineering Design | Unit 1
Big Ideas
1
Engineering sketches are thinking tools, not art assignments.
2
A sketch captures design intent before time is spent building or modeling.
3
Good sketches make ideas easier to compare, discuss, and improve.
Ask yourself: What would someone else understand from my sketch or documentation?

## Slide 7
LOCKWOODSTEM
Lesson 1.1
Why Engineers Sketch
Use these moves while you work
LockwoodSTEM | Introduction to Engineering Design | Unit 1
Key Moves
Move | What it means
Capture the idea | Sketch the main form before details are added.
Label the function | Show what each feature is supposed to do.
Communicate intent | Use notes and arrows so another person understands the idea.

## Slide 8
LOCKWOODSTEM
Lesson 1.1
Why Engineers Sketch
What you should have by the end of the lesson
LockwoodSTEM | Introduction to Engineering Design | Unit 1
Evidence Checklist
□
Date and title the sketch page
□
Use light construction lines first
□
Add object lines and labels
□
Explain the design purpose in words
□
Save evidence in your notebook
End-of-Lesson Product
A dated engineering sketch that communicates a design idea clearly enough for another person to understand.
Ask yourself: Could another student understand what I did today without me explaining it out loud?

## Slide 9
LOCKWOODSTEM
Lesson 1.2
Line Conventions
LockwoodSTEM | Introduction to Engineering Design | Unit 1
How do different types of lines help engineers communicate clearly?
Lesson 1.2
Line Conventions
Connect today’s work to your engineering notebook evidence.

## Slide 10
LOCKWOODSTEM
Lesson 1.2
Line Conventions
Big ideas you should understand before you start the work
LockwoodSTEM | Introduction to Engineering Design | Unit 1
Big Ideas
1
Line types are part of the language of engineering drawings.
2
Object, construction, hidden, center, and dimension lines each have a job.
3
Line weight helps readers tell planning marks from final design geometry.
Ask yourself: What would someone else understand from my sketch or documentation?

## Slide 11
LOCKWOODSTEM
Lesson 1.2
Line Conventions
Use these moves while you work
LockwoodSTEM | Introduction to Engineering Design | Unit 1
Key Moves
Move | What it means
Construction lines | Use light lines to plan size, alignment, and spacing.
Object lines | Use dark lines for visible edges and final geometry.
Special lines | Use hidden, center, and dimension lines only when they add information.

## Slide 12
LOCKWOODSTEM
Lesson 1.2
Line Conventions
What you should have by the end of the lesson
LockwoodSTEM | Introduction to Engineering Design | Unit 1
Evidence Checklist
□
Practice at least three line types
□
Label each line type
□
Use correct line weight
□
Apply lines to an aerospace-style part
□
Correct unclear or inconsistent lines
End-of-Lesson Product
A line convention practice sketch showing the correct purpose and appearance of major technical line types.
Ask yourself: Could another student understand what I did today without me explaining it out loud?

## Slide 13
LOCKWOODSTEM
Lesson 1.3
Object Lines & Hidden Lines
LockwoodSTEM | Introduction to Engineering Design | Unit 1
How can a sketch show features that cannot be seen from one view?
Lesson 1.3
Object Lines & Hidden Lines
Connect today’s work to your engineering notebook evidence.

## Slide 14
LOCKWOODSTEM
Lesson 1.3
Object Lines & Hidden Lines
Big ideas you should understand before you start the work
LockwoodSTEM | Introduction to Engineering Design | Unit 1
Big Ideas
1
Object lines show visible edges and surfaces.
2
Hidden lines show important internal or blocked features.
3
Hidden lines should clarify geometry, not clutter the view.
Ask yourself: What would someone else understand from my sketch or documentation?

## Slide 15
LOCKWOODSTEM
Lesson 1.3
Object Lines & Hidden Lines
Use these moves while you work
LockwoodSTEM | Introduction to Engineering Design | Unit 1
Key Moves
Move | What it means
Visible edges | Darken only the edges that can be seen from the chosen view.
Hidden features | Use short dashed lines for holes, slots, or edges behind surfaces.
Clean drawing | Avoid adding hidden lines unless they help the viewer understand the part.

## Slide 16
LOCKWOODSTEM
Lesson 1.3
Object Lines & Hidden Lines
What you should have by the end of the lesson
LockwoodSTEM | Introduction to Engineering Design | Unit 1
Evidence Checklist
□
Identify visible edges
□
Add hidden lines where needed
□
Keep hidden lines lighter than object lines
□
Explain what hidden features represent
□
Revise confusing sketches
End-of-Lesson Product
A technical sketch using object and hidden lines to communicate visible and non-visible features.
Ask yourself: Could another student understand what I did today without me explaining it out loud?

## Slide 17
LOCKWOODSTEM
Lesson 1.4
Centerlines & Symmetry
LockwoodSTEM | Introduction to Engineering Design | Unit 1
How do engineers show the center of a feature or object in a technical sketch?
Lesson 1.4
Centerlines & Symmetry
Connect today’s work to your engineering notebook evidence.

## Slide 18
LOCKWOODSTEM
Lesson 1.4
Centerlines & Symmetry
Big ideas you should understand before you start the work
LockwoodSTEM | Introduction to Engineering Design | Unit 1
Big Ideas
1
Centerlines mark axes, centers, and symmetry.
2
Circular features and repeated patterns need center references.
3
Centerlines help parts align during modeling, fabrication, and inspection.
Ask yourself: What would someone else understand from my sketch or documentation?

## Slide 19
LOCKWOODSTEM
Lesson 1.4
Centerlines & Symmetry
Use these moves while you work
LockwoodSTEM | Introduction to Engineering Design | Unit 1
Key Moves
Move | What it means
Find the center | Mark the center of holes, arcs, cylinders, or repeated features.
Show symmetry | Use centerlines to communicate that two sides mirror each other.
Support dimensions | Place dimensions from reliable center references when needed.

## Slide 20
LOCKWOODSTEM
Lesson 1.4
Centerlines & Symmetry
What you should have by the end of the lesson
LockwoodSTEM | Introduction to Engineering Design | Unit 1
Evidence Checklist
□
Add centerlines to holes or circular features
□
Show symmetry where appropriate
□
Use centerlines consistently
□
Label alignment purpose
□
Check that centerlines do not look like object lines
End-of-Lesson Product
A sketch that uses centerlines to show hole centers, axes, or symmetry clearly.
Ask yourself: Could another student understand what I did today without me explaining it out loud?

## Slide 21
LOCKWOODSTEM
Lesson 1.5
Isometric Sketching
LockwoodSTEM | Introduction to Engineering Design | Unit 1
How can engineers show a 3D object clearly on a flat page?
Lesson 1.5
Isometric Sketching
Connect today’s work to your engineering notebook evidence.

## Slide 22
LOCKWOODSTEM
Lesson 1.5
Isometric Sketching
Big ideas you should understand before you start the work
LockwoodSTEM | Introduction to Engineering Design | Unit 1
Big Ideas
1
Isometric sketches show width, height, and depth at the same time.
2
Edges follow consistent vertical and angled directions.
3
Proportion and alignment matter more than artistic shading at first.
Ask yourself: What would someone else understand from my sketch or documentation?

## Slide 23
LOCKWOODSTEM
Lesson 1.5
Isometric Sketching
Use these moves while you work
LockwoodSTEM | Introduction to Engineering Design | Unit 1
Key Moves
Move | What it means
Start with a box | Build the object inside a simple width-height-depth envelope.
Follow axes | Keep vertical edges vertical and depth/width edges at consistent angles.
Add features | Place cuts, holes, and details after the main form is correct.

## Slide 24
LOCKWOODSTEM
Lesson 1.5
Isometric Sketching
What you should have by the end of the lesson
LockwoodSTEM | Introduction to Engineering Design | Unit 1
Evidence Checklist
□
Create an isometric box or envelope
□
Use consistent isometric axes
□
Add visible edges and features
□
Label the part or design intent
□
Check proportions before darkening lines
End-of-Lesson Product
A clean isometric sketch that communicates a 3D object using consistent axes and visible features.
Ask yourself: Could another student understand what I did today without me explaining it out loud?

## Slide 25
LOCKWOODSTEM
Lesson 1.5
Isometric Drawing Video Connection
Optional video connection
LockwoodSTEM | Introduction to Engineering Design | Unit 1
Video Connection
Isometric Drawing - Simplified
Watch for: • how the isometric axes are used • how a 3D form starts from simple shapes • how proportion and alignment guide the sketch
Scan or Open
Open Video
https://www.youtube.com/watch?v=c_NRuzPs9R8

## Slide 26
LOCKWOODSTEM
Lesson 1.6
Isometric Circles, Arcs, and Shading
LockwoodSTEM | Introduction to Engineering Design | Unit 1
How can engineers show curved features and surface depth in an isometric sketch?
Lesson 1.6
Isometric Circles, Arcs, and Shading
Connect today’s work to your engineering notebook evidence.

## Slide 27
LOCKWOODSTEM
Lesson 1.6
Isometric Circles, Arcs, and Shading
Big ideas you should understand before you start the work
LockwoodSTEM | Introduction to Engineering Design | Unit 1
Big Ideas
1
Circles usually appear as ellipses in isometric view.
2
Curved features need careful placement so they still look attached to the part.
3
Shading and value can show surface direction, depth, and form.
Ask yourself: What would someone else understand from my sketch or documentation?

## Slide 28
LOCKWOODSTEM
Lesson 1.6
Isometric Circles, Arcs, and Shading
Use these moves while you work
LockwoodSTEM | Introduction to Engineering Design | Unit 1
Key Moves
Move | What it means
Curved features | Sketch circles, holes, and arcs as ellipses that follow the surface.
Surface value | Use light, medium, and dark values to show different faces.
Clarity first | Use shading to support the sketch, not hide weak geometry.

## Slide 29
LOCKWOODSTEM
Lesson 1.6
Isometric Circles, Arcs, and Shading
What you should have by the end of the lesson
LockwoodSTEM | Introduction to Engineering Design | Unit 1
Evidence Checklist
□
Practice at least one curved feature
□
Use a light-to-dark value scale
□
Add shading to show form
□
Keep object edges readable
□
Explain what the curved feature represents
End-of-Lesson Product
An isometric sketch with at least one curved feature and shading that improves form clarity.
Ask yourself: Could another student understand what I did today without me explaining it out loud?

## Slide 30
LOCKWOODSTEM
Lesson 1.7
Orthographic Projection
LockwoodSTEM | Introduction to Engineering Design | Unit 1
Why do engineers use multiple 2D views instead of only one 3D sketch?
Lesson 1.7
Orthographic Projection
Connect today’s work to your engineering notebook evidence.

## Slide 31
LOCKWOODSTEM
Lesson 1.7
Orthographic Projection
Big ideas you should understand before you start the work
LockwoodSTEM | Introduction to Engineering Design | Unit 1
Big Ideas
1
Orthographic projection shows a 3D object as multiple flat views.
2
Each view shows only two dimensions at a time.
3
Multiple views reduce guessing when shape, size, or hidden features matter.
Ask yourself: What would someone else understand from my sketch or documentation?

## Slide 32
LOCKWOODSTEM
Lesson 1.7
Orthographic Projection
Use these moves while you work
LockwoodSTEM | Introduction to Engineering Design | Unit 1
Key Moves
Move | What it means
Choose views | Use front, top, and right-side views to show the important features.
Align views | Keep matching widths, heights, and depths lined up.
Compare with 3D | Use the isometric view to check if each 2D view makes sense.

## Slide 33
LOCKWOODSTEM
Lesson 1.7
Orthographic Projection
What you should have by the end of the lesson
LockwoodSTEM | Introduction to Engineering Design | Unit 1
Evidence Checklist
□
Identify front, top, and right views
□
Align the views correctly
□
Show matching features across views
□
Use hidden lines if needed
□
Check the views against the 3D object
End-of-Lesson Product
A basic orthographic layout that shows front, top, and right-side views of the same object.
Ask yourself: Could another student understand what I did today without me explaining it out loud?

## Slide 34
LOCKWOODSTEM
Lesson 1.7
Orthographic Projection Video Connection
Optional video connection
LockwoodSTEM | Introduction to Engineering Design | Unit 1
Video Connection
Beginning Orthographic Projection
Watch for: • how front, top, and side views relate • how 3D features become 2D views • how alignment keeps views accurate
Scan or Open
Open Video
https://www.youtube.com/watch?v=ytwEDvX-l44

## Slide 35
LOCKWOODSTEM
Lesson 1.8
Top, Front & Right Side Views
LockwoodSTEM | Introduction to Engineering Design | Unit 1
How do engineers keep multiple views of the same object organized and accurate?
Lesson 1.8
Top, Front & Right Side Views
Connect today’s work to your engineering notebook evidence.

## Slide 36
LOCKWOODSTEM
Lesson 1.8
Top, Front & Right Side Views
Big ideas you should understand before you start the work
LockwoodSTEM | Introduction to Engineering Design | Unit 1
Big Ideas
1
View placement is standardized so drawings are easy to read.
2
The front view anchors the drawing layout.
3
Matching dimensions must align across related views.
Ask yourself: What would someone else understand from my sketch or documentation?

## Slide 37
LOCKWOODSTEM
Lesson 1.8
Top, Front & Right Side Views
Use these moves while you work
LockwoodSTEM | Introduction to Engineering Design | Unit 1
Key Moves
Move | What it means
Front view | Choose the view that best shows the part shape and function.
Top view | Place it directly above the front view and keep widths aligned.
Right view | Place it directly to the right and keep heights aligned.

## Slide 38
LOCKWOODSTEM
Lesson 1.8
Top, Front & Right Side Views
What you should have by the end of the lesson
LockwoodSTEM | Introduction to Engineering Design | Unit 1
Evidence Checklist
□
Choose the best front view
□
Place top and right views correctly
□
Project matching edges across views
□
Keep spacing neat and readable
□
Label views if needed
End-of-Lesson Product
A multiview sketch with correctly placed and aligned front, top, and right-side views.
Ask yourself: Could another student understand what I did today without me explaining it out loud?

## Slide 39
LOCKWOODSTEM
Lesson 1.9
Dimensioning Basics
LockwoodSTEM | Introduction to Engineering Design | Unit 1
How do engineers show the size of an object clearly in a drawing?
Lesson 1.9
Dimensioning Basics
Connect today’s work to your engineering notebook evidence.

## Slide 40
LOCKWOODSTEM
Lesson 1.9
Dimensioning Basics
Big ideas you should understand before you start the work
LockwoodSTEM | Introduction to Engineering Design | Unit 1
Big Ideas
1
Views show shape, but dimensions show size.
2
Dimension lines, extension lines, arrows, and numbers work together.
3
Good dimensioning avoids missing, repeated, or confusing measurements.
Ask yourself: What would someone else understand from my sketch or documentation?

## Slide 41
LOCKWOODSTEM
Lesson 1.9
Dimensioning Basics
Use these moves while you work
LockwoodSTEM | Introduction to Engineering Design | Unit 1
Key Moves
Move | What it means
Dimension lines | Show the distance being measured with arrowheads.
Extension lines | Connect the measurement to the feature without touching the object line.
Readable values | Place numbers clearly and include units when required.

## Slide 42
LOCKWOODSTEM
Lesson 1.9
Dimensioning Basics
What you should have by the end of the lesson
LockwoodSTEM | Introduction to Engineering Design | Unit 1
Evidence Checklist
□
Add overall size dimensions
□
Add feature location dimensions
□
Use extension and dimension lines correctly
□
Avoid duplicate dimensions
□
Check that someone could model the part from your drawing
End-of-Lesson Product
A dimensioned technical sketch that communicates the size and important feature locations of a part.
Ask yourself: Could another student understand what I did today without me explaining it out loud?

## Slide 43
LOCKWOODSTEM
Lesson 1.9
Dimensioning Video Connection
Optional video connection
LockwoodSTEM | Introduction to Engineering Design | Unit 1
Video Connection
Engineering Drawing Dimensioning: The Basics Explained
Watch for: • how dimensions communicate size • how extension and dimension lines work • why drawings should avoid missing or duplicate dimensions
Scan or Open
Open Video
https://www.youtube.com/watch?v=Q9kOFtUltqM

## Slide 44
LOCKWOODSTEM
Lesson 1.10
Aerospace Bracket Sketch
LockwoodSTEM | Introduction to Engineering Design | Unit 1
How can sketches communicate the shape, features, and size of a part before it is modeled or built?
Lesson 1.10
Aerospace Bracket Sketch
Connect today’s work to your engineering notebook evidence.

## Slide 45
LOCKWOODSTEM
Lesson 1.10
Aerospace Bracket Sketch
Big ideas you should understand before you start the work
LockwoodSTEM | Introduction to Engineering Design | Unit 1
Big Ideas
1
A bracket holds, supports, connects, or aligns other parts.
2
Aerospace brackets often balance strength, light weight, mounting holes, and clearances.
3
A technical sketch should show form, features, and dimensions together.
Ask yourself: What would someone else understand from my sketch or documentation?

## Slide 46
LOCKWOODSTEM
Lesson 1.10
Aerospace Bracket Sketch
Use these moves while you work
LockwoodSTEM | Introduction to Engineering Design | Unit 1
Key Moves
Move | What it means
Study the part | Identify holes, supports, cutouts, ribs, and mounting features.
Sketch the form | Use isometric or multiview sketches to show shape clearly.
Add dimensions | Dimension key features needed for CAD or fabrication.

## Slide 47
LOCKWOODSTEM
Lesson 1.10
Aerospace Bracket Sketch
What you should have by the end of the lesson
LockwoodSTEM | Introduction to Engineering Design | Unit 1
Evidence Checklist
□
Create a bracket sketch
□
Label major features
□
Include important dimensions
□
Use line conventions accurately
□
Explain the bracket function
End-of-Lesson Product
A clear aerospace bracket sketch with labels, dimensions, and line conventions.
Ask yourself: Could another student understand what I did today without me explaining it out loud?

## Slide 48
LOCKWOODSTEM
Lesson 1.11
Rocket Assembly Reverse Engineering
LockwoodSTEM | Introduction to Engineering Design | Unit 1
How can engineers learn from an existing rocket assembly by carefully taking it apart?
Lesson 1.11
Rocket Assembly Reverse Engineering
Connect today’s work to your engineering notebook evidence.

## Slide 49
LOCKWOODSTEM
Lesson 1.11
Rocket Assembly Reverse Engineering
Big ideas you should understand before you start the work
LockwoodSTEM | Introduction to Engineering Design | Unit 1
Big Ideas
1
Reverse engineering means studying an existing product to understand how it works.
2
Each rocket part has a function, fit, and relationship to other parts.
3
Careful disassembly protects evidence and makes reassembly possible.
Ask yourself: What would someone else understand from my sketch or documentation?

## Slide 50
LOCKWOODSTEM
Lesson 1.11
Rocket Assembly Reverse Engineering
Use these moves while you work
LockwoodSTEM | Introduction to Engineering Design | Unit 1
Key Moves
Move | What it means
Observe first | Record the assembled rocket before removing parts.
Disassemble carefully | Separate parts without damaging connections or losing orientation.
Document fits | Note where parts slide, press, align, or connect.

## Slide 51
LOCKWOODSTEM
Lesson 1.11
Rocket Assembly Reverse Engineering
What you should have by the end of the lesson
LockwoodSTEM | Introduction to Engineering Design | Unit 1
Evidence Checklist
□
Photograph or sketch the assembled rocket
□
List major parts
□
Record how parts connect
□
Note any fit or alignment issues
□
Keep parts organized for reassembly
End-of-Lesson Product
A reverse-engineering notebook entry showing rocket parts, functions, fits, and initial observations.
Ask yourself: Could another student understand what I did today without me explaining it out loud?

## Slide 52
LOCKWOODSTEM
Lesson 1.12
Why Documentation Matters
LockwoodSTEM | Introduction to Engineering Design | Unit 1
Why is a design not finished when the sketch or model is finished?
Lesson 1.12
Why Documentation Matters
Connect today’s work to your engineering notebook evidence.

## Slide 53
LOCKWOODSTEM
Lesson 1.12
Why Documentation Matters
Big ideas you should understand before you start the work
LockwoodSTEM | Introduction to Engineering Design | Unit 1
Big Ideas
1
Documentation explains what the design is, how it works, and how it was built.
2
Good documentation makes work repeatable and inspectable.
3
Missing notes make future design decisions harder to justify.
Ask yourself: What would someone else understand from my sketch or documentation?

## Slide 54
LOCKWOODSTEM
Lesson 1.12
Why Documentation Matters
Use these moves while you work
LockwoodSTEM | Introduction to Engineering Design | Unit 1
Key Moves
Move | What it means
Record context | Explain what the part or assembly is supposed to do.
Record evidence | Include sketches, measurements, photos, and observations.
Record decisions | Explain why a design choice or revision makes sense.

## Slide 55
LOCKWOODSTEM
Lesson 1.12
Why Documentation Matters
What you should have by the end of the lesson
LockwoodSTEM | Introduction to Engineering Design | Unit 1
Evidence Checklist
□
Add clear titles and dates
□
Use labels and captions
□
Record part names and functions
□
Explain connection methods
□
Identify what evidence is still missing
End-of-Lesson Product
A documentation update that makes the rocket assembly understandable without verbal explanation.
Ask yourself: Could another student understand what I did today without me explaining it out loud?

## Slide 56
LOCKWOODSTEM
Lesson 1.13
Measurement Tools
LockwoodSTEM | Introduction to Engineering Design | Unit 1
How do engineers choose the right tool for accurate measurement?
Lesson 1.13
Measurement Tools
Connect today’s work to your engineering notebook evidence.

## Slide 57
LOCKWOODSTEM
Lesson 1.13
Measurement Tools
Big ideas you should understand before you start the work
LockwoodSTEM | Introduction to Engineering Design | Unit 1
Big Ideas
1
Different measurement tools are accurate for different tasks.
2
A measurement is only useful if the tool, units, and method are clear.
3
Repeated measurements help identify mistakes or variation.
Ask yourself: What would someone else understand from my sketch or documentation?

## Slide 58
LOCKWOODSTEM
Lesson 1.13
Measurement Tools
Use these moves while you work
LockwoodSTEM | Introduction to Engineering Design | Unit 1
Key Moves
Move | What it means
Ruler / tape | Use for overall lengths and rough layout.
Calipers | Use for inside, outside, depth, and step measurements.
Micrometer | Use for precise thickness or diameter when needed.

## Slide 59
LOCKWOODSTEM
Lesson 1.13
Measurement Tools
What you should have by the end of the lesson
LockwoodSTEM | Introduction to Engineering Design | Unit 1
Evidence Checklist
□
Choose the correct measuring tool
□
Record units and tool used
□
Take repeated measurements
□
Measure at least one critical rocket feature
□
Note uncertainty or variation
End-of-Lesson Product
A measurement table for rocket parts that includes tool choice, units, and repeated measurements.
Ask yourself: Could another student understand what I did today without me explaining it out loud?

## Slide 60
LOCKWOODSTEM
Lesson 1.13
Measurement Tools Video Connection
Optional video connection
LockwoodSTEM | Introduction to Engineering Design | Unit 1
Video Connection
How to Properly Use Calipers
Watch for: • outside, inside, and depth measurements • why the tool should be zeroed • how to avoid squeezing or tilting the jaws
Scan or Open
Open Video
https://www.youtube.com/watch?v=pIy3pIn53Ls

## Slide 61
LOCKWOODSTEM
Lesson 1.14
Tolerances
LockwoodSTEM | Introduction to Engineering Design | Unit 1
Why do engineers allow some variation in measurements, but not too much?
Lesson 1.14
Tolerances
Connect today’s work to your engineering notebook evidence.

## Slide 62
LOCKWOODSTEM
Lesson 1.14
Tolerances
Big ideas you should understand before you start the work
LockwoodSTEM | Introduction to Engineering Design | Unit 1
Big Ideas
1
A target dimension is the intended size of a feature.
2
Tolerance is the allowed variation around that target.
3
Fit decisions depend on whether variation still allows the assembly to work.
Ask yourself: What would someone else understand from my sketch or documentation?

## Slide 63
LOCKWOODSTEM
Lesson 1.14
Tolerances
Use these moves while you work
LockwoodSTEM | Introduction to Engineering Design | Unit 1
Key Moves
Move | What it means
Target value | Identify the intended size or fit.
Acceptable range | Set upper and lower limits that still allow function.
Fit decision | Decide pass, adjust, or redesign based on evidence.

## Slide 64
LOCKWOODSTEM
Lesson 1.14
Tolerances
What you should have by the end of the lesson
LockwoodSTEM | Introduction to Engineering Design | Unit 1
Evidence Checklist
□
Identify one target dimension
□
Create an acceptable tolerance range
□
Compare measured values to the range
□
Classify the fit result
□
Explain what should change if the fit fails
End-of-Lesson Product
A tolerance analysis showing whether a rocket part fit is acceptable, too loose, or too tight.
Ask yourself: Could another student understand what I did today without me explaining it out loud?

## Slide 65
LOCKWOODSTEM
Lesson 1.15
Adhesives & Fasteners
LockwoodSTEM | Introduction to Engineering Design | Unit 1
How do engineers decide the best way to connect parts together?
Lesson 1.15
Adhesives & Fasteners
Connect today’s work to your engineering notebook evidence.

## Slide 66
LOCKWOODSTEM
Lesson 1.15
Adhesives & Fasteners
Big ideas you should understand before you start the work
LockwoodSTEM | Introduction to Engineering Design | Unit 1
Big Ideas
1
Connections can be permanent, removable, adjustable, or temporary.
2
Adhesives can be quick but may make disassembly difficult.
3
Fasteners and fit-based features can support inspection, repair, and revision.
Ask yourself: What would someone else understand from my sketch or documentation?

## Slide 67
LOCKWOODSTEM
Lesson 1.15
Adhesives & Fasteners
Use these moves while you work
LockwoodSTEM | Introduction to Engineering Design | Unit 1
Key Moves
Move | What it means
Choose connection purpose | Decide if the part must be removed later.
Match method to load | Consider strength, alignment, and expected forces.
Document the method | Record whether the connection slides, snaps, presses, glues, or fastens.

## Slide 68
LOCKWOODSTEM
Lesson 1.15
Adhesives & Fasteners
What you should have by the end of the lesson
LockwoodSTEM | Introduction to Engineering Design | Unit 1
Evidence Checklist
□
Identify rocket connection points
□
Classify each connection method
□
Decide removable vs. permanent
□
Explain one connection trade-off
□
Update assembly notes
End-of-Lesson Product
A connection method table for the rocket assembly that explains how parts attach and why.
Ask yourself: Could another student understand what I did today without me explaining it out loud?

## Slide 69
LOCKWOODSTEM
Lesson 1.16
Rocket Assembly Systems
LockwoodSTEM | Introduction to Engineering Design | Unit 1
How do multiple rocket parts work together as one assembly?
Lesson 1.16
Rocket Assembly Systems
Connect today’s work to your engineering notebook evidence.

## Slide 70
LOCKWOODSTEM
Lesson 1.16
Rocket Assembly Systems
Big ideas you should understand before you start the work
LockwoodSTEM | Introduction to Engineering Design | Unit 1
Big Ideas
1
A part is one individual component of a larger design.
2
A subassembly is a smaller group of parts that work together.
3
The full assembly depends on alignment, fit, order, and function.
Ask yourself: What would someone else understand from my sketch or documentation?

## Slide 71
LOCKWOODSTEM
Lesson 1.16
Rocket Assembly Systems
Use these moves while you work
LockwoodSTEM | Introduction to Engineering Design | Unit 1
Key Moves
Move | What it means
Part names | Use consistent names for each component.
Subassemblies | Group related parts such as fin section, payload bay, or nose section.
System function | Explain how the parts work together as one rocket assembly.

## Slide 72
LOCKWOODSTEM
Lesson 1.16
Rocket Assembly Systems
What you should have by the end of the lesson
LockwoodSTEM | Introduction to Engineering Design | Unit 1
Evidence Checklist
□
Identify all major rocket parts
□
Group parts into subassemblies
□
Describe the function of each part
□
Mark connection points
□
Explain the full assembly purpose
End-of-Lesson Product
A rocket system map showing parts, subassemblies, connection points, and functions.
Ask yourself: Could another student understand what I did today without me explaining it out loud?

## Slide 73
LOCKWOODSTEM
Lesson 1.17
Documenting the Rocket Assembly
LockwoodSTEM | Introduction to Engineering Design | Unit 1
What information does someone need to understand or recreate the rocket assembly?
Lesson 1.17
Documenting the Rocket Assembly
Connect today’s work to your engineering notebook evidence.

## Slide 74
LOCKWOODSTEM
Lesson 1.17
Documenting the Rocket Assembly
Big ideas you should understand before you start the work
LockwoodSTEM | Introduction to Engineering Design | Unit 1
Big Ideas
1
Assembly documentation combines labeled sketches, part names, materials, and connection notes.
2
The goal is clarity for a future builder or reviewer.
3
Photos and sketches should be labeled with what they prove.
Ask yourself: What would someone else understand from my sketch or documentation?

## Slide 75
LOCKWOODSTEM
Lesson 1.17
Documenting the Rocket Assembly
Use these moves while you work
LockwoodSTEM | Introduction to Engineering Design | Unit 1
Key Moves
Move | What it means
Assembly sketch | Show the rocket assembled with labeled parts.
Parts list | Name each part and record quantity/material notes.
Connection notes | Explain how each part fits, aligns, or attaches.

## Slide 76
LOCKWOODSTEM
Lesson 1.17
Documenting the Rocket Assembly
What you should have by the end of the lesson
LockwoodSTEM | Introduction to Engineering Design | Unit 1
Evidence Checklist
□
Create a labeled assembly sketch
□
Add a clear parts list
□
Write connection notes
□
Include material or fabrication notes
□
Identify missing documentation
End-of-Lesson Product
A labeled rocket assembly documentation page that explains parts, connections, materials, and purpose.
Ask yourself: Could another student understand what I did today without me explaining it out loud?

## Slide 77
LOCKWOODSTEM
Lesson 1.18
Rocket Exploded View
LockwoodSTEM | Introduction to Engineering Design | Unit 1
How can engineers show rocket parts separated without losing how they fit together?
Lesson 1.18
Rocket Exploded View
Connect today’s work to your engineering notebook evidence.

## Slide 78
LOCKWOODSTEM
Lesson 1.18
Rocket Exploded View
Big ideas you should understand before you start the work
LockwoodSTEM | Introduction to Engineering Design | Unit 1
Big Ideas
1
An exploded view separates parts so each component can be seen.
2
Alignment should still show where parts belong in the assembly.
3
Exploded views can communicate assembly order and fit relationships.
Ask yourself: What would someone else understand from my sketch or documentation?

## Slide 79
LOCKWOODSTEM
Lesson 1.18
Rocket Exploded View
Use these moves while you work
LockwoodSTEM | Introduction to Engineering Design | Unit 1
Key Moves
Move | What it means
Separate along axis | Move parts away from the assembly without changing orientation.
Show alignment | Keep parts visually lined up with where they fit.
Add labels | Use part names, callouts, or item numbers for clarity.

## Slide 80
LOCKWOODSTEM
Lesson 1.18
Rocket Exploded View
What you should have by the end of the lesson
LockwoodSTEM | Introduction to Engineering Design | Unit 1
Evidence Checklist
□
Create a rocket exploded view
□
Keep parts aligned
□
Label each part clearly
□
Show assembly order if possible
□
Connect view to BOM item names
End-of-Lesson Product
A rocket exploded view showing separated parts, alignment, and clear part labels.
Ask yourself: Could another student understand what I did today without me explaining it out loud?

## Slide 81
LOCKWOODSTEM
Lesson 1.19
Rocket Bill of Materials
LockwoodSTEM | Introduction to Engineering Design | Unit 1
How do engineers keep track of every part needed to build an assembly?
Lesson 1.19
Rocket Bill of Materials
Connect today’s work to your engineering notebook evidence.

## Slide 82
LOCKWOODSTEM
Lesson 1.19
Rocket Bill of Materials
Big ideas you should understand before you start the work
LockwoodSTEM | Introduction to Engineering Design | Unit 1
Big Ideas
1
A Bill of Materials is a structured list of all parts in an assembly.
2
Quantities must match the actual number of parts used.
3
Notes can explain materials, connections, or special features.
Ask yourself: What would someone else understand from my sketch or documentation?

## Slide 83
LOCKWOODSTEM
Lesson 1.19
Rocket Bill of Materials
Use these moves while you work
LockwoodSTEM | Introduction to Engineering Design | Unit 1
Key Moves
Move | What it means
Item number | Give each part a consistent number or name.
Quantity | Count repeated parts such as fins, rings, or fasteners accurately.
Notes | Record materials, fit type, or special assembly details.

## Slide 84
LOCKWOODSTEM
Lesson 1.19
Rocket Bill of Materials
What you should have by the end of the lesson
LockwoodSTEM | Introduction to Engineering Design | Unit 1
Evidence Checklist
□
List every rocket part
□
Record quantity for each item
□
Add material or fabrication notes
□
Match item names to exploded view labels
□
Check for missing repeated parts
End-of-Lesson Product
A complete rocket Bill of Materials that matches the exploded view and assembly notes.
Ask yourself: Could another student understand what I did today without me explaining it out loud?

## Slide 85
LOCKWOODSTEM
Lesson 1.20
Rocket Assembly Notes
LockwoodSTEM | Introduction to Engineering Design | Unit 1
How do engineers write reassembly instructions that another team can follow?
Lesson 1.20
Rocket Assembly Notes
Connect today’s work to your engineering notebook evidence.

## Slide 86
LOCKWOODSTEM
Lesson 1.20
Rocket Assembly Notes
Big ideas you should understand before you start the work
LockwoodSTEM | Introduction to Engineering Design | Unit 1
Big Ideas
1
Assembly notes explain order, alignment, fit, and cautions.
2
Good instructions reduce mistakes during rebuilding.
3
Notes should include checks that confirm a step was done correctly.
Ask yourself: What would someone else understand from my sketch or documentation?

## Slide 87
LOCKWOODSTEM
Lesson 1.20
Rocket Assembly Notes
Use these moves while you work
LockwoodSTEM | Introduction to Engineering Design | Unit 1
Key Moves
Move | What it means
Build order | Write the sequence from first part to final assembly.
Alignment checks | Explain how parts should line up before connecting.
Caution notes | Identify fragile parts, tight fits, or places where force should not be used.

## Slide 88
LOCKWOODSTEM
Lesson 1.20
Rocket Assembly Notes
What you should have by the end of the lesson
LockwoodSTEM | Introduction to Engineering Design | Unit 1
Evidence Checklist
□
Write a clear assembly sequence
□
Include alignment instructions
□
Describe connection methods
□
Add at least one caution note
□
Check if another team could follow the notes
End-of-Lesson Product
A set of rocket assembly notes that would allow another student to reassemble the rocket accurately.
Ask yourself: Could another student understand what I did today without me explaining it out loud?

## Slide 89
LOCKWOODSTEM
Lesson 1.21
Engineering Change Requests
LockwoodSTEM | Introduction to Engineering Design | Unit 1
How do engineers document a proposed design change without losing control of the original design?
Lesson 1.21
Engineering Change Requests
Connect today’s work to your engineering notebook evidence.

## Slide 90
LOCKWOODSTEM
Lesson 1.21
Engineering Change Requests
Big ideas you should understand before you start the work
LockwoodSTEM | Introduction to Engineering Design | Unit 1
Big Ideas
1
An Engineering Change Request records a proposed improvement.
2
The change should be supported by measurements, fit issues, documentation, or feedback.
3
A change affects parts, materials, assembly order, cost, or performance.
Ask yourself: What would someone else understand from my sketch or documentation?

## Slide 91
LOCKWOODSTEM
Lesson 1.21
Engineering Change Requests
Use these moves while you work
LockwoodSTEM | Introduction to Engineering Design | Unit 1
Key Moves
Move | What it means
State the problem | Describe what does not work as well as it should.
Use evidence | Support the change with sketches, measurements, tolerance data, or observations.
Explain impact | Identify what the change affects and what should improve.

## Slide 92
LOCKWOODSTEM
Lesson 1.21
Engineering Change Requests
What you should have by the end of the lesson
LockwoodSTEM | Introduction to Engineering Design | Unit 1
Evidence Checklist
□
Identify one rocket assembly improvement
□
Use evidence to justify the change
□
Describe the proposed revision
□
Explain impact on parts or assembly
□
Complete an ECR-style summary
End-of-Lesson Product
An Engineering Change Request proposing one rocket assembly improvement supported by evidence.
Ask yourself: Could another student understand what I did today without me explaining it out loud?

## Slide 93
LOCKWOODSTEM
Lesson 1.22
Final Rocket Assembly Proposal Presentation
LockwoodSTEM | Introduction to Engineering Design | Unit 1
How can a team justify a proposed rocket assembly improvement using engineering evidence?
Lesson 1.22
Final Rocket Assembly Proposal Presentation
Connect today’s work to your engineering notebook evidence.

## Slide 94
LOCKWOODSTEM
Lesson 1.22
Final Rocket Assembly Proposal Presentation
Big ideas you should understand before you start the work
LockwoodSTEM | Introduction to Engineering Design | Unit 1
Big Ideas
1
A design proposal should connect the original assembly, evidence, and recommended change.
2
Strong presentations explain both strengths and limitations.
3
Engineering communication should be clear, honest, and evidence-based.
Ask yourself: What would someone else understand from my sketch or documentation?

## Slide 95
LOCKWOODSTEM
Lesson 1.22
Final Rocket Assembly Proposal Presentation
Use these moves while you work
LockwoodSTEM | Introduction to Engineering Design | Unit 1
Key Moves
Move | What it means
Explain the assembly | Describe the original rocket parts, fits, and function.
Show evidence | Use sketches, measurements, BOM, exploded view, and ECR evidence.
Make a recommendation | State the proposed improvement and why it matters.

## Slide 96
LOCKWOODSTEM
Lesson 1.22
Final Rocket Assembly Proposal Presentation
What you should have by the end of the lesson
LockwoodSTEM | Introduction to Engineering Design | Unit 1
Evidence Checklist
□
Organize the final documentation package
□
Prepare evidence slides or talking points
□
Include the proposed change
□
Explain the expected benefit
□
Practice a clear design conclusion
End-of-Lesson Product
A final rocket assembly improvement proposal supported by sketches, measurements, BOM, exploded view, assembly notes, and ECR evidence.
Ask yourself: Could another student understand what I did today without me explaining it out loud?

## Slide 97
Unit 1 Close
You now have the visual communication tools needed to sketch, measure, document, and propose improvements to aerospace assemblies.
Next: Unit 2 turns sketches and measurements into CAD models and 3D printed parts.