## Slide 1
IED UNIT 2 • LESSON 2.8
Fillets, Chamfers, and Design Intent
FOCUS QUESTION
How do edge features improve function, safety, and printability?
SELECT
SOFTEN
JUSTIFY
Parametric CAD and Part Design
Model • Check • Print • Recommend

## Slide 2
MISSION BRIEFING
45-Minute Flight Plan
A full lesson to build CAD evidence for the Unit 2 tolerance tester.
LockwoodSTEM | Introduction to Engineering Design | Unit 2
Lesson 2.8
Learning targets
• Distinguish between fillets and chamfers. • Apply edge features intentionally. • Explain how edge treatment affects function or manufacturing.
Success looks like…
Your edge features have a reason beyond appearance.
Agenda + pacing
5 min
Opening prompt
7 min
CAD concept + vocabulary
8 min
Interactive vote
10 min
Guided modeling/application
8 min
Scenario and quick check
5 min
Portfolio evidence
2 min
Exit debrief

## Slide 3
OPENING PROMPT
When might rounding an edge make a part worse instead of better?
Think first. Then be ready to share one short answer.
LockwoodSTEM | Introduction to Engineering Design | Unit 2
Lesson 2.8
Quick response
Write or think silently for one minute, then share a response that connects today’s CAD skill to accuracy, editability, or printability.
We will reveal a useful way to think about this on the next slide.

## Slide 4
OPENING DEBRIEF
A CAD Thinking Move
Use the answer as a starting point for today’s modeling work.
LockwoodSTEM | Introduction to Engineering Design | Unit 2
Lesson 2.8
If the edge controls fit, alignment, or contact with another part, changing it without a reason can reduce accuracy or function.
SELECT
SOFTEN
JUSTIFY
Carry-forward idea: your CAD choices should be controlled enough to revise and clear enough to explain.

## Slide 5
INTERACTIVE VOTE
Which explanation shows design intent?
Vote first. Then justify your choice before the reveal.
LockwoodSTEM | Introduction to Engineering Design | Unit 2
Lesson 2.8
A
I added fillets because they look nice
B
I filleted the hand-contact edge to reduce sharpness
C
I changed every edge randomly
D
I added chamfers because the menu was available
Vote first. Then we will reveal the strongest engineering choice.

## Slide 6
VOTE REVEAL
Best Answer
The strongest answer connects to controlled CAD practice.
LockwoodSTEM | Introduction to Engineering Design | Unit 2
Lesson 2.8
Best answer: B
I filleted the hand-contact edge to reduce sharpness
Why it fits
It connects the feature to a function: safer handling.
Carry-forward idea
In Unit 2, the strongest CAD decisions improve accuracy, editability, printability, or evidence quality.

## Slide 7
CAD SKILL
What We Are Practicing
These are the big ideas behind today’s work.
LockwoodSTEM | Introduction to Engineering Design | Unit 2
Lesson 2.8
Key idea 1
Fillets and chamfers can improve safety, strength, fit, and printability.
Key idea 2
Edge treatment should support the function, not just appearance.
Key idea 3
Design intent explains why a feature exists.
Ask yourself: How does this CAD decision improve accuracy, editability, or printability?

## Slide 8
MODELING WORKFLOW
Use These Moves
The goal is a cleaner model and stronger evidence.
LockwoodSTEM | Introduction to Engineering Design | Unit 2
Lesson 2.8
Modeling moves
1
Identify edges that need treatment.
2
Apply fillets or chamfers with reasonable sizes.
3
Avoid changing critical fit surfaces without a reason.
Quality checks
• Does the model match the intended measurements? • Can another student understand the feature? • Will the part be printable or testable?
Good CAD work is controlled enough to revise and clear enough to explain.

## Slide 9
STUDENT TASK
Apply the Skill
Use the presentation and your CAD workspace together.
LockwoodSTEM | Introduction to Engineering Design | Unit 2
Lesson 2.8
Add intentional edge features to a model and label the design reason for each.
Checkpoint: be ready to show your CAD evidence before the exit ticket.

## Slide 10
KEY IDEA
Claim + CAD Evidence
Every CAD choice should leave evidence another person can inspect.
LockwoodSTEM | Introduction to Engineering Design | Unit 2
Lesson 2.8
Claim
What you believe about the model
CAD Evidence
The feature, dimension, screenshot, setting, or test that supports the claim
Decision
What you do next because of the evidence
Evidence can include sketches, dimensions, constraints, screenshots, exported files, slicer previews, measurements, and fit tests.

## Slide 11
MINI CHALLENGE
What Evidence Would You Need?
Select the evidence that would best support the claim.
LockwoodSTEM | Introduction to Engineering Design | Unit 2
Lesson 2.8
Claim: “My fillets, chamfers, and design intent work is accurate and ready to move forward.”
A
A screenshot or model view that shows the feature
B
A statement that it looks good
C
Relevant dimensions, settings, or test results
D
A random file name
Vote for the two strongest pieces of evidence.

## Slide 12
EVIDENCE REVEAL
Strongest Evidence
The best evidence connects directly to the claim.
LockwoodSTEM | Introduction to Engineering Design | Unit 2
Lesson 2.8
Best support: A + C
A screenshot/model view shows what was created. Dimensions, settings, or test results show whether it meets the requirement.
Useful, but not enough alone
Opinions, appearance, and file names may support the story, but they do not prove the model is correct by themselves.

## Slide 13
SCENARIO RESPONSE
What Should the Engineer Do Next?
Choose the strongest next step and explain your reasoning.
LockwoodSTEM | Introduction to Engineering Design | Unit 2
Lesson 2.8
A student fillets a peg that must fit tightly into a hole. What should they consider?
A
Whether the fillet changes the fit surface
B
Whether the part looks more advanced
C
Whether the timeline is longer
D
Whether the file saves faster
Vote first. Then we will reveal the strongest next step.

## Slide 14
SCENARIO REVEAL
Best Next Step
The best move turns uncertainty into useful evidence.
LockwoodSTEM | Introduction to Engineering Design | Unit 2
Lesson 2.8
Best answer: A — Whether the fillet changes the fit surface
Record what happened
Capture the issue or result clearly.
Identify the likely cause
Connect the issue to a CAD decision.
Revise or confirm the model
Make a controlled change or document why no change is needed.
Save evidence for the portfolio
Keep proof of the decision.

## Slide 15
QUICK CHECK
Evidence or Opinion?
Vote first. Then explain which statement is strongest and why.
LockwoodSTEM | Introduction to Engineering Design | Unit 2
Lesson 2.8
A
“My fillets, chamfers, and design intent model is good because it looks finished.”
Vote: evidence or opinion?
B
“The model uses the documented dimension and the screenshot shows the controlled feature.”
Vote: evidence or opinion?
C
“I revised the model after the check showed a size or fit problem.”
Vote: evidence or opinion?

## Slide 16
QUICK CHECK REVEAL
Evidence or Opinion?
A strong engineering answer connects a claim to specific evidence.
LockwoodSTEM | Introduction to Engineering Design | Unit 2
Lesson 2.8
A: Opinion-heavy
Uses a vague judgment: “looks finished.”
B: Evidence-based
Connects the model to a documented dimension and visible feature evidence.
C: Evidence-based reasoning
Connects a revision to a specific check result or problem.
Takeaway: claim + specific CAD evidence = stronger engineering communication.

## Slide 17
PORTFOLIO EVIDENCE
What You Save Today
Save the strongest artifact from today for your Unit 2 portfolio.
LockwoodSTEM | Introduction to Engineering Design | Unit 2
Lesson 2.8
Deliverable checklist
• Part includes intentional edge treatment. • Student explains why each treatment was added. • Critical dimensions are still protected.
Portfolio evidence
• Dated notebook entry • Screenshot or exported file • Short claim explaining what the evidence proves
Your final portfolio should show how the model improved across the unit.

## Slide 18
MISSION DEBRIEF
Exit Ticket
Show that you understand the skill before moving forward.
LockwoodSTEM | Introduction to Engineering Design | Unit 2
Lesson 2.8
1
One CAD decision you made or checked today
2
One piece of evidence that proves your model is controlled, accurate, or printable
3
One question you still have about today’s tool, workflow, or assignment
Next mission: Lesson 2.9 — Revolve Features: Nose Cone and Nozzle