## Slide 1
POE 1.2
Simple Machines
in Aerospace Systems
How do simple machines change force, distance, direction, or motion in aerospace applications?

## Slide 2
Lesson Mission
LockwoodSTEM | Principles of Engineering | Unit 1
02
Today’s mission
Identify simple machines in aerospace mechanisms and explain what useful change each one creates.
By the end, you should be able to…
• Name the six simple machines.
• Connect each one to an aerospace mechanism.
• Describe the input → output change.
• Create a concept sketch that explains the change.
Key idea
Simple machines do not create energy. They change how force or motion is applied.

## Slide 3
Part A: The Six Simple Machines
LockwoodSTEM | Principles of Engineering | Unit 1
04
Simple machines change something useful
They trade force, distance, direction, or motion so a mechanism can complete a task.
INPUT
SIMPLE
MACHINE
OUTPUT
force / motion enters
change happens
useful result

## Slide 4
Part A: Reference Set
LockwoodSTEM | Principles of Engineering | Unit 1
05
The six simple machines
Use these as your answer bank for Part B.
1
Lever
rotates about a fulcrum
2
Pulley
changes pull direction
3
Wheel & axle
changes torque, force, or speed
4
Inclined plane
trades distance for lower input force
5
Wedge
separates, cuts, or locks
6
Screw
turns rotation into linear motion

## Slide 5
Part B: Identify the Simple Machine
LockwoodSTEM | Principles of Engineering | Unit 1
06
Mechanism snapshots
For each one, ask: What goes in? What changes? Why is that useful?
Wheel & axle
Rover drive
Input → machine → output
Screw
Solar panel deployment
Input → machine → output
Pulley
Cargo bay hoist
Input → machine → output
Wedge / lever
Separation or release
Input → machine → output

## Slide 6
Part C: Ideal Mechanical Advantage
LockwoodSTEM | Principles of Engineering | Unit 1
07
IMA compares useful geometry
In Part C and Part D, you use ideal geometry and ignore friction.
Lever
IMA = effort arm / resistance arm
Pulley
IMA = supporting rope segments
Wheel & axle
IMA = wheel radius / axle radius
Inclined plane
IMA = ramp length / height
Wedge
IMA = wedge length / thickness
Screw
IMA = circumference / lead
Key idea
Higher IMA usually means more force advantage, but it also requires a distance or speed tradeoff.

## Slide 7
Part C: Ideal Mechanical Advantage
LockwoodSTEM | Principles of Engineering | Unit 1
07

## Slide 8
Part D: Guided IMA Examples
LockwoodSTEM | Principles of Engineering | Unit 1
08
Set up the calculation before solving
These match the first three calculation types on the worksheet.
Lever
Access hatch handle
IMA = effort arm / resistance arm
IMA = 0.48 m / 0.12 m = 4
Pulley
Instrument hoist
IMA = supporting rope segments
IMA = 4
Wheel & axle
Rover drive
IMA = wheel radius / axle radius
IMA = 0.18 m / 0.03 m = 6

## Slide 9
Part D: More IMA Examples
LockwoodSTEM | Principles of Engineering | Unit 1
09
Distance tradeoffs show up in different ways
Look carefully at which dimensions belong in the ratio.
Inclined plane
Payload ramp
IMA = ramp length / height
IMA = 2.40 m / 0.60 m = 4
Wedge
Separation tool
IMA = wedge length / thickness
IMA = 80 mm / 20 mm = 4
Screw
Precision actuator
IMA = 2πr / lead
IMA = 2π(40 mm) / 2.0 mm ≈ 126

## Slide 10
Part E: Input, Output, and Tradeoffs
LockwoodSTEM | Principles of Engineering | Unit 1
10
Describe what changes
Your worksheet responses should connect motion to a mission need.
Input
What force or motion enters the mechanism?
Output
What useful force or motion leaves the mechanism?
Tradeoff
What is gained, and what is sacrificed?
Key idea
Use words like force, torque, speed, distance, direction, linear motion, or rotation.

## Slide 11
Part F: Mission Need Matching
LockwoodSTEM | Principles of Engineering | Unit 1
11
Choose the best starting mechanism
Justify the match by naming the tradeoff.
A
Move a heavy package into a test stand
Limited input force → inclined plane or pulley
Explain why it fits.
B
Extend a landing support slowly
Precision + high force → screw
Explain why it fits.
C
Drive a rover over rough terrain
Torque at ground → wheel & axle
Explain why it fits.
D
Change cable direction around structure
Route force safely → pulley
Explain why it fits.

## Slide 12
Part G: Recommendation Evidence
LockwoodSTEM | Principles of Engineering | Unit 1
12
Recommend a mechanism using evidence
Your final response combines identification, IMA, and engineering reasoning.
Mission scenario
A lunar rover must lift a sealed 12 kg sample container 0.30 m into protected storage. The mechanism must be compact, predictable, and avoid sudden motion.
Your evidence should include:
• recommended simple machine
• input and desired output
• one IMA calculation
• one tradeoff or test needed

## Slide 13
Part H: Exit Check
LockwoodSTEM | Principles of Engineering | Unit 1
13
Before you submit today
Use this checklist to verify your worksheet is complete.
Exit check
1. Define ideal mechanical advantage.
2. Name the best simple machine for precise linear motion.
3. Explain why higher IMA usually requires a tradeoff.
Turn in
Completed 1.2 Worksheet Added To ENB